## Slide 1: Minimon v2.3.0
New Features 08/2013

## Slide 2: P11 derivates support
Integration of 6 additional types
  P11 MRplus
  P11 MR2
  P11 HE
  P11 F
  P11 LE
  P11 ULE
Default Kernel configurable in mctypes.dat

## Slide 3: Scripting
New control structures
  if / else / endif
  while / endw
  do / loop until
Labels introduced
  GOTO Label:
  Label:
Former fixed loop command supported as well
if %5=4
_message ”it’s 4"
else
_message ”it’s not 4"
endif
while %4<8
_message %4
_assign %4= %4+1
endw
do
_message “%4 is “,%4
_assign %4= %4+1
loop until %4=5
goto END2:
END1:
_message “end1“
END2:
_message “end2”

## Slide 4: Variables
Support of up to 100 variables: %00 to %99
Variables have always numeric type
Variables can be used in expressions for control structures (if, while, do)
Assign values to variables using _assign
_assign supports also: timer, rnd16, rnd8
_assign %0=3A
_assign %1=SYSCON
_assign %2=TIMER
_assign %3=RND8
_assign %99=RND16
  if %1=100
  ...
  while %1>100
  ...
  do
  ...
  loop until %1<=50

## Slide 5: New script commands (1)
_print: output of strings, variables,SFRs in log
_input: input of variable values
_delayms: Wait 1-n ms
_poll: block script execution until value in target memory is reached
_print “script ended successfully”
_print “value: “,%5
_print “SYSCON: “,SYSCON
_input “please enter value:”,%6
_delayms 200

## Slide 6: New script commands (2)
_r16: read word from target memory
_w16: write word to target memory
_d16: download word from dump memory into target memory (different address)
_u16: upload word from target memory into dump memory (different address)
; direct adressing
_w16 E00002,2222
_r16 E00002
_d16 E00002,E00022
_u16 E00002,E00022
_poll E00002,FFFF,2222
; indirect adressing
_assign %1=E00002
_assign %2=E00022
_w16 %1,2222
_r16 %1
_d16 %1,%2
_u16 %1,%2
_poll %1,FFFF,2222

## Slide 7: File types
More flexibility for Intel Hex
  empty lines, comments
  warning on checksum validation
Support for SRE File format
  types: 19, 28, 37
  via menu
  via commandline/scripts
    _loadsre <filename>
    _savesre <filename>
#this is a testfile
:020000040000FA
:20000000B488944A4DC603C2D0B50B69DCCA5FF6DF0EF35D86C40D97774C9FA54347D4D397 # comment
:20004000A2352F951475E742C9604AEBA1A06D198FB1E9D5058BEA6EAD8083765A67450E0E
:00000001FF

## Slide 8: Frontend
Support up to 256 Com Ports (patched MS Comm OCX required) – no official feature
  max. Portnumber configurable in preferences file
Scaling of Frontend GUI possible for larger display

## Slide 9: Open
Flash testing / assembly buffer features
Multiple selections
Fill commands
Relocatable P11 kernel