## Slide 1: Minimon
Concept overview

## Slide 2: Minimon
Tiny monitor program started via Bootstrap
Rich client Windows application („Frontend“)
Key features
  Hex Editor
  Memory transfer
  Flash operations
  Load and start user code
  SFR viewing and editing
  Scripting

## Slide 3: Frontend overview
Memory Window
SFR Window
Terminal/Status Window
Command line
Menu
Toolbar

## Slide 4: Minimon
Memory window: view, edit, exchange (download, upload, compare, flash) with target memory
SFR window: add/remove SFRs for watching, edit values, group in up to 8 tabs
Terminal/Status window: log output of called operations and results
Command line: enter shell commands

## Slide 5: Memory Window

## Slide 6: Target configuration
Supported families: C16x, XC16x, XC2xxx
Currently 44 supported microcontroller types
Differences in
  Kernel (per family, but also special full featured and k-line)
  Memory definition: internal RAM and flash memory
  SFR definition
Target can be configured related to
  Microcontroller type (selects kernel, memory and SFR definitions)
  Clock rate (important for baud rate changes during established communication)
  SFR and generic registers to initialize
  Additional (external) memory sections to configure
    Selection of flash drivers for external flashes
  Calling of EINIT after boot

## Slide 7: Target configuration

## Slide 8: Interface configuration
Frontend and kernel communicate via RS232
Restricted baud rates during boot (depending on mc type and clock rate) from 1200 baud to 38400 baud
Baudrate can be changed later on
Support of COM1-COM16 with default Microsoft MSCOMM32.OCX
Support of COM1-COM256 with patched OCX
Support of KLINE (-> requires proper Kernel)

## Slide 9: Kernel configuration
Different kernels for each family
Different kernels for KLINE
Different kernels for different feature sets
  Default: most important features
  Full: additional special features: ASC0toASC1, Writeseq, Setprotection
  Autobaud: supporting Pegasus Autobaud feature
All kernels are relocatable to other memory sections (relative jumps only)
Kernel could also be embedded in user code

## Slide 10: Kernels & features
Minimon Kernels |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
v3.0.1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NAME | FAMILY | KLINE | LOADERACK | AUTOBAUD | LOCATION |  | RELOCATABLE | WRITEWORD | WRITEBLOCK | READBLOCK | CALL | JMP | EINIT | SWRESET | GETCHECKSUM | TEST | READWORD | WRITESEQ | ASC02ASC1 | SETPROTECTION
C16X_DEFAULT | C16X |  | x |  | 00FA60 | 00FBE7 | x | x | x | x | x | x | x | x | x | x | x |  |  | 
C16X_KLINE | C16X | x | x |  | 00FA60 | 00FBE9 | x | x | x | x | x | x | x | x | x | x | x |  |  | 
C16X_FULL | C16X |  | x |  | 00FA60 | 00FC09 | x | x | x | x | x | x | x | x | x | x | x | x |  | 
C16X_AUTOBAUD_FULL | C16X |  | x | x | 00FA60 | 00FC49 | x | x | x | x | x | x | x | x | x | x | x | x |  | 
XC16X_DEFAULT | XC16X |  | x |  | E00024 | E001AB | x | x | x | x | x | x | x | x | x | x | x |  |  | 
XC16X_KLINE | XC16X | x | x |  | E00024 | E001AD | x | x | x | x | x | x | x | x | x | x | x |  |  | 
XC16X_FULL | XC16X |  | x |  | E00024 | E0026D | x | x | x | x | x | x | x | x | x | x | x | x | x | x
XC16X_AUTOBAUD_FULL | XC16X |  | x | x | E00024 | E002B5 | x | x | x | x | x | x | x | x | x | x | x | x | x | x
XC2000_DEFAULT | XC2XXX |  |  |  | E00020 | E001CD | x | x | x | x | x | x | x | x | x | x | x |  |  | 
XC2000_KLINE | XC2XXX | x |  |  | E00020 | E001D1 | x | x | x | x | x | x | x | x | x | x | x |  |  | 
XC2000_KLINE_STEPA11 | XC2XXX | x |  |  | E00020 | E0001D1 | x | x | x | x | x | x | x | x | x | x | x |  |  | 
P11_U_LE_KLINE | XC2XXX | x |  |  | E00020 | E0001E1 | x | x | x | x | x | x | x | x | x | x | x |  |  | 

## Slide 11: Other configurations
Terminal: ASCII or HEX mode (default is ASCII, but for user code HEX mode could be helpful)
Frontend: Set colors, regular SFR refresh, enable logging, blank character
and: windows scale