## Slide 1: Minimon
New features in v3.0.1

## Slide 2: Overview
Scripting: Improved control structures
  If/else
  while
  do loop until
  labels
Improved variable usage
File handling (Intel Hex improved, SRE introduced)
New shell/script commands
  input and output
  script control: delaysms, poll
  upload and download of 16 bit words
  selection handling
  assembly buffer features
  dump memory manipulation commands
Frontend improvements
  Scalable frontend
  Support COM1-COM256
  SFR Window: enlarged, 8 tabs

## Slide 3: Variables
Support of up to 100 variables: %00 to %99
Variables have always numeric type (6 Bytes hexadecimal)
Variables can be used in many shell commands
Variables can be used in expressions for control structures (if, while, do)
Assign values to variables using _assign
_assign supports also: timer, rnd16, rnd8

## Slide 4: Variables - Assign
_assign: Assigns an expression into a variable
possible syntax:
  _assign <v>=<x>
  _assign <v>=<o1><x>
  _assign <v>=<x><o2><y>
  <v>.. variable %00-%99
  <x>,<y>..
  variable or
  SFR name or
  constant (24 bit hex) or
  special enum TIMER, RND8, RND16
  <o2>.. binary operator + - * / & | ^ >> << #
  <o1>.. unary operator ~
Examples:
_assign %1=00003D
_assign %99=SYSCON
_assign %5=~%2
_assign %3=%3+1
_assign %1=timer
_assign %2=rnd8
_assign %3=rnd16
_assign %3=%1&%2
_assign %3=%1|%2
_assign %3=%1^%2
_assign %2=%1<<2
_assign %2=%1>>2
_assign %1=5/9
_assign %1=5#9

## Slide 5: File handling
Intel Hex file improvements
  Comments, empty lines supported
  Warning on checksum validation
Support of SRE File format
  Supported file types: 19, 28, 37
  via menu
  via commandline/scripts
    _loadsre <filename>
    _savesre <filename>
Indexed filename saving: _savex
Relative path handling with _setpath

## Slide 6: File handling
COMMAND | PARAMETERS | DESCRIPTION
_loadsre | <filename>, | loads SR file <Filename> into host memory
_savesre | <filename>,<recordsize> optional,<format> optional | saves selection into SRE file <Filename>. <Recordsize> in bytes, <format> can be 19, 28 or 37.
_setpath | <type>,<path> | sets base path <path> for file operation type <type>. <type> can be SAVE, LOAD, SCRIPT or LOG by default, all types have Minimon installation path as base path if full path is provided with an operation, the base path is ignored
_savex | <filename>,<variable>,<recordsize> optional,<format> optional | Save selection to intel hex file. Filename is extended by file index provided by variable

## Slide 7: Input and output, script control
_print: output of strings, variables,timestamp, SFRs in log
  _writelogfile: equivalent to _print but unconditional write
_input: input of variable values, yes/no option
  _viewascii
_delayms: Wait 1-n ms
_poll: block script execution until value in target memory is reached

## Slide 8: Input and output, script control
_poll | <target memory address>¦<variable>,<data mask>¦<variable>,<value>¦<variable> | Blocks script execution until word on target memory equals expected value
_input <string>,<variable> | <string>,<variable> | Display message box and wait for input of a hex value into a variable
_delayms | <delay time>¦<variable> | delays for <delay time> miliseconds. Alternatively, wait ms given in variable
_logfile | ON¦OFF¦<variable> | turns the log file writing on or off
_writelogfile | <string>¦<SFR>¦<variable>[,<string>¦<SFR>¦<variable> optional...] | writes information to log file, can be string, SFR or variable
_print | <string>¦<SFR>¦<variable>[,<string>¦<SFR>¦<variable> optional...] | prints information to log window and log file, can be string, SFR or variable
_viewascii | <byteswap> | Views the current selection as ascii text and writes to Terminal view as well as log file. If <byteswap> is 1, MSB is printed first

## Slide 9: Upload and download
_r16: read word from target memory
_w16: write word to target memory
_d16: download word from dump memory into target memory (different address)
_u16: upload word from target memory into dump memory (different address)
_upload: optionally upload sub-selection only

## Slide 10: Upload and download
COMMAND | PARAMETERS | DESCRIPTION
_upload | <selection index>¦<variable> optional | reads from target memory into selection. If parameter <selection index> is passed, only selection with this index is upload. Selection index is decimal value
_r16 | <Address>¦<variable> | Read a data word from target memory address
_w16 | <Address>¦<variable>,<Data>¦<variable> | Write a data word to target memory address
_d16 | dump memory address>¦<variable>,<target memory address>¦<variable> | Write a data word to from dump memory address to target memory address
_u16 | <target memory address>¦<variable>,<dump memory address>¦<variable> | Write a data word to from target memory address to dump memory address

## Slide 11: Selections
_moveselection: move sub-selection
_removeselection: remove sub-selection
COMMAND | PARAMETERS | DESCRIPTION
_addselection | <start address>¦<variable>, <end address>¦<variable> | adds selection from start address to end address, addresses can be passed as constants or variables
_clearselections | - | removes all selections
_showselections | - | lists the current selections and their range
_moveselection | <selection index>¦<variable>, <displacement>¦<variable> | Shift selection number <selection index> by <displacement> bytes. Selection index can also be in variable, as well as displacement. Selection index is decimal value
_removeselection | <selection index>¦<variable> | Remove selection number <selection index> from selection, selection index can also be in variable Selection index is decimal value

## Slide 12: Assembly buffer features
_downloadASB
_loadasb_byte
_loadasb_word
_downloadtoasb | - | Download data into the flash assembly buffer from selection.
_loadasb_byte | RND8¦<data byte>¦variable,<count> optional | Download bytewise data into the flash assembly buffer, can be random number, constant value or variable content.
_loadasb_word | RND16¦<data byte>¦variable,<count> optional | Download wordwise data into the flash assembly buffer, can be random number, constant value or variable content.

## Slide 13: Dump memory manipulation
_dumpmemecc: dumps data from target memory into selection
_dumpmodify: modifys selection content
_dumpmemecc | <maddr>¦<variable>,<dummyrd>¦<variable> optional,<clrstat>¦<variable> optional,<incstep>¦<variable> optional | Dumps 16 bit value from target <maddr> into selection. Starts at smallest selection address and increments dump memory address by 16 bits. If parameter <dummyrd> is provided with 1, a dummy read is performed on current dump memory address before reading from <address>. If parameter <clrstat> is provided with 1, a clear status sequence is executed after reading from <address>. If parameter <incstep> is provided, a different increment of dump memory address than 16 bits can be used. XC16x needs 8 byte increment for 64bit data to read each 8bit ECC. P11 has 16 byte data for each 9bit ECC.
_dumpmodify | <XOR-Mask>¦<variable>, <AND-Mask>¦<variable>, <OR-Mask>¦<variable>, <RotateRight>¦<variable> optional, <incstep>¦<variable> optional | 16bit wise data modification within the virtual dump that is selected: #data16bit:=(((#data16bit ^ XORMask) & ANDMask )¦ OR-Mask) >> #Rotate16bitRight

## Slide 14: Frontend improvements
Scalable Frontend (e.g. 150%)
Larger SFR window
Support of 8 SFR Tabs