## Slide 1: Minimon
Frontend-Kernel Communication

## Slide 2: Overview
Communication via RS232 / optionally KLINE
3 interesting phases
  Boot Process
  Regular communication
  Driver called

## Slide 3: Boot process
Frontend sends Byte 0 to Microcontroller
Microcontroller‘s Bootstrap loader (BSL) evaluates baudrate and sends back Identifier
Frontend sends 32 Bytes Loader
Microcontroller writes loader into internal RAM and executes it
Loader acknowledges successful start with Byte 0x01 (not in XC2xxx because there is no space left for sending command)
Frontend sends minimon kernel to loader
Loader receives kernel, writes it into internal RAM and executes it
Kernel acknowledges successful start with 0x03
-> Kernel is started successfully
Frontend
Microcontroller

## Slide 4: Regular communication
Communication pattern:
  Communication is always initiated by Frontend by sending a Function code
  Kernel answers with acknowledge 0xAA
  Frontend sends parameters (optional)
  Kernel executes the command
  Kernel sends back return parameters (optional)
  Kernel sends back acknowledge 0xEA

## Slide 5: Regular communication
(function code) 
(acknowledge 1=AAh) 
(parameters)
(return parameters) 
(acknowledge 2=EAh)
Name | Funct.C. | Parameters | Return Parameters
Write Word | 82h | 3 Bytes address (LSB first) 2 Bytes value (LSB first) | None
Write Block of Bytes | 84h | 3 Bytes startaddress (LSB first) 2 Bytes length, (LSB first) <length> bytes values | None
Read Block of Bytes | 85h | 3 Bytes startaddress, (LSB first) 2 Bytes length (LSB first) | <length> bytes values
Monitor Ext. Interface* (Call Subroutine) | 9Fh | 3 Bytes program start address (LSB f.) 8 Word parameters R8-R15 (LSB f.) | 8 Word parameters R8-R15 (LSB f.)
Simple Go Command | 41h | 3 Bytes program start address (LSB f.) | None
Execute EINIT | 31h | None | None
Execute SWRESET | 32h | None | None
Get Checksum | 33h | None | 1 Word checksum
Test of Communication | 93h | None | None
ASC0 to ASC1 | CCh | None | None
Read Word | CDh | 3 Bytes startaddress, (LSB first) | 2 Bytes value (LSB first)
Write Word Sequence | CEh | 3 Bytes buffer start address (LSB f.) 1 Byte buffer length | None
Set protection | D1h | 1 Byte password 1 Byte new password 1 Byte protection level | None

## Slide 6: Driver Handling
General pattern:
  Frontend downloads driver into target memory (via command _download)
  Frontend uses function _call (= kernels monitor extension interface (9F)) to execute driver
  Kernel executes driver, if successfully finished, returns 0xEA. Frontend is blocking waiting for successful termination
  -> If driver is struggled or takes too long, Frontend will run into timeout

## Slide 7: Flash programming
General pattern:
  Frontend checks if driver is already downloaded
  If not, it downloads it into target memory (via _download)
  Frontend writes desired contents of current flash page into buffer area of internal ram (usually FC80-FCFF, configurable in MEM file)
  Frontend uses function monitor extension interface (9F) to execute driver and passes parameters in R8-R15 (e.g. driver function code, target address, buffer address)
  Kernel calls driver
  Driver executes function and returns
  If successfully finished, Kernel returns 0xEA

## Slide 8: User code execution
Driver interface can also be used to execute routines
Parameters and return parameters could be passed via R8-R15
If bigger parameter size is needed, use concept as in flash driver with buffer address
Routines should not take too long, otherwise Frontend times out (but could be reconnected. Workaround: disconnect, delay and reconnect)
Example: Routine which counts bits in a specific area of the internal RAM

## Slide 9: How to write your own driver
Driver interface can also be used to execute own routines
Parameters and return parameters should be passed via R8-R15
If bigger parameter size is needed, use concept as in flash driver with buffer address
Routine execution should not take too long, otherwise Frontend times out (but could be reconnected. Workaround: disconnect, delay and reconnect)
User code must always terminated with RETS, because it has been called with CALLS
Use assembler for user code due to better control about overhead, stack etc.

## Slide 10: Example
FC_01 EQU 0001h ; Function code 1
FC_02 EQU 0002h ; Function code 2
Init: ; Do some initialization if required
Cmd1:
CMP R8,#(FC_01)
JMPR cc_NE,Cmd2
; Add here your code for Function 01
RETS
Cmd2:
CMP R8,#(FC_02)
JMPR cc_NE,Cmd3
; Add here your code for Function 02
RETS
Cmd3: ; No further Function
RETS
RETV ; RET virtual

## Slide 11: Calling example in Frontend
_connect NOPROMPT
_load example.hex
_download
_call E00300,0001 ;assuming example is located at E00300 on build
.. results are listed here