## Slide 1: Minimon
Scripting

## Slide 2: Overview
Scripts are using shell commands and optionally control structures
Simplest form of script is a text file with shell commands
Scripts can be executed via
  Menu
  Toolbar (up to 8 user script buttons)
  Commandline (Minimon starts and executes automatically script)
Scripts can call subscripts (maximum depth=3)
Usage of variables is necessary if using control structures
Scripts are limited to 5000 lines per script file

## Slide 3: Variables
Support of up to 100 variables: %00 to %99
Variables have always numeric type (6 Bytes hexadecimal)
Variables can be used in many shell commands
Variables can be used in expressions for control structures (if, while, do)
Assign values to variables using _assign
_assign supports also: timer, rnd16, rnd8

## Slide 4: Variables - Assign
_assign: Assigns an expression into a variable
possible syntax:
  _assign <v>=<x>
  _assign <v>=<o1><x>
  _assign <v>=<x><o2><y>
  <v>.. variable %00-%99
  <x>,<y>..
  variable or
  SFR name or
  constant (24 bit hex) or
  special enum TIMER, RND8, RND16
  <o2>.. binary operator + - * / & | ^ >> << #
  <o1>.. unary operator ~
Examples:
_assign %1=00003D
_assign %99=SYSCON
_assign %5=~%2
_assign %3=%3+1
_assign %1=timer
_assign %2=rnd8
_assign %3=rnd16
_assign %3=%1&%2
_assign %3=%1|%2
_assign %3=%1^%2
_assign %2=%1<<2
_assign %2=%1>>2
_assign %1=5/9
_assign %1=5#9

## Slide 5: Control structures
If/else/end if: conditional execution
while/endw:
do loop until
labels and goto: define labels which can be jumped to with goto command
if %4=2
_message „%4 is 2"
if %5=5
_message „%5 is 5"
else
_message „%5 is not 5"
endif
endif
_assign %4=5
while %4<8
_print “%4 is not yet 8"
_assign %4=%4+1
endw
_print "0"
L1:
_print "1"
GOTO L3:
L2:
_print "2"
GOTO L4:
L3:
_print "3"
GOTO L2:
L4:
_print "4"
_assign %4=5
do
_print “%4 is not yet 8"
_assign %4=%4+1
loop until %4=8

## Slide 6: Condition expressions
Used in if, while and do loop
Syntax: <x><c><y>
  <x>,<y> can be
  variable
  SFR name
  constant (hexadecimal 24 bit)
  <c> is comparison operator out of
  = > < >= <= <>

## Slide 7: Commands influencing script ex.
_pause: pauses script execution until OK pressed
_input: pauses script execution until requested value is entered
_delay: delays for seconds passed
_delayms: delays for miliseconds passed
_executescript: calls subscript
_quit: terminates Minimon
_poll: blocks script execution by polling target memory until it reaches passed value

## Slide 8: Script File handling
Last executed scripts are put to script history in menue
Subscripts are not put to script history
with _setpath SCRIPT,<path>, a relative path for _executescript command can be set
Script history, user scripts and script path is stored in preferences file
-> use preferences file for workspace handling

## Slide 9: Exercises
Write a script which connects to a target, randomly fills 16 bytes in targets internal RAM, uploads it and counts the number of bits set to 1. Ask if output shall be performed and print result into log file.